## Slide 1: Data Link Layer
Prepared By: Ms. Vidhi Pandya

## Slide 2: Learning objectives
To understand design principle of Data Link Layer
To understand Different algorithms
To understand error and flow control
To understand different protocols

## Slide 3: Error Detection & Correction
Telephone system – 3 Parts
      Switches
      Interoffice Trunks
      Local Loops – error rate is high

## Slide 4: Error – correcting codes
Strategies
Include enough redundant information along with each block of data sent
Include only enough redundancy to allow receiver to deduce that an error occurred

## Slide 5: Understanding of error
Continue …..
Consider the following things
      M – data bits / message bits
      R – redundant / check bits
      N – Total length
      N = M + R Codeword

## Slide 6
Continue …..
Consider we have 2 codewords
10001001 and 10110001
To determine how many bits differ – apply X-OR
1 0 0 0 1 0 0 1
1 0 1 1 0 0 0 1
0 0 1 1 1 0 0 0
The number of bit positions in which two codewords differ is known as Hamming Distance (d)

## Slide 7: Error Detection Techniques
Techniques
      Single Parity Check
      CRC – Cyclic Redundancy Check
      Checksum

## Slide 8: Single Parity Check
Odd Parity Check
Continue …..
Even Parity Check
If No of 1’s in data are odd then add 0 at the end as odd parity bit
If No of 1’s in data are even then add 1 at the end as odd parity bit to convert No of 1’s in a odd number
If No of 1’s in data are odd then add 1 at the end as even parity bit to convert No of 1’s in a even number
If No of 1’s in data are even then add 0 at the end as even parity bit
For Example : Data Stream – 110110 and Odd Parity is used
To transfer these data stream from sender side to receiver side, sender will add the parity bit at that last of data stream. Here, No of 1’s are 4 i.e. even number so datalink layer of sender side will add 1 as a odd parity bit and transfer the stream to receiver side.
No at receiver side, data stream will be checked and calculate the parity bit. If both calculated and sent parity bit match then there is no error otherwise there is a single bit error

## Slide 9
Data Unit :
1 | 0 | 0 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 1
+
+
+
0 | 1 | 1 | 1 | 1 | 1 | 0 | 0
1
1
1
1
0
1
0 | 1 | 1 | 1 | 1 | 1 | 1 | 0
1’s com
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1
Sender Side
Continue …..
Checksum
10011001100010001001101011000001

## Slide 10
1 | 0 | 0 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 1
+
+
+
1
1’s com
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1
+
1 | 1 | 1 | 1 | 1 | 1 | 0 | 1
1
1
1
0
1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Continue …..
Receiver Side
Data Unit :
10011001100010001001101011000001
Checksum:
10000001

## Slide 11
Data Unit :
Continue …..
CRC
1101011011
G(x) Generator:
10011
11010110110000
10011
10011
110000101
010011
10011
0000010110
10011
0010100
10011
001110
Sent Stream :
11010110111110
Sender Side
Receiver Side
110000101
10011
11010110111110
10011
010011
10011
0000010111
10011
0010011
10011
00000
Note : At the receiver side, there is no remainder so we can say that the data stream which is received is error free.

## Slide 12: Reference Book: Computer Networks 4th edition Andrew s. tanenbaum