## Slide 1: OSPF – Open Shortest Path First
Interior gateway routing protocol
A routing algorithm within autonomous system is called interior gateway routing protocol
OSPF supports 3 kinds of connections and n/w
  Point-to-point lines between exactly two routers
  Multiaccess n/ws with broadcasting
  Multiaccess n/ws without broadcasting

## Slide 2
Large Ases is divided in to numbered areas, where area is a n/w or set of contiguous n/ws.
An area is a generalization of subnet
Outside an area, its topology and details are not visible
Every AS has a backbone area, called area 0
All areas are connected to backbone, possibly by tunnels
During normal operation, 3 kinds of routes may be needed
  Intra-area
  Interarea
  Inter-AS

## Slide 3
Intra-area routes are the easiest
  3 steps:- go from source to backbone
go across backbone to destination area
go to destination
This algo forces star configuration on OSPF with backbone being hub and other areas being spokes

## Slide 4
5 types of messages in OSPF

## Slide 5: BGP – Border Gateway Protocol
Exterior gateway routing protocol
n/w grouped into one o three categories
  1. stub n/w : only one connection to BGP graph
  2. multiconnected n/w
  3. transit n/w : willing to handle third party packets, possibly with some restrictions and usually for pay
  TCP connection