## Slide 1
Bansari Patel
Teaching cum. Research Assistant
Computer Science and Engineering
03-01-2022
SDN Basics and Open Flow
CS374 –MODERN NETWORKS
DECEMBER 2021– JULY 2022

## Slide 2
SDN architecture
SDN data plane
SDN data plane network device
OpenFlow logical network device
OpenFlow environment
OpenFlow switch
OpenFlow versions
Chapter Objectives

## Slide 3
Control and Data Plane

## Slide 4
Traditional network is very inflexible
  It is requires all the network devices to implement the same protocol for communication
However in SDN the central controller performs complex functionalities like routing, naming, policies and security.
Separation of data and control plane
Control plane is implemented in controller
SDN controller has a centralized view of the network
Open interfaces are defined between the devices
The network is programmable by applications
SDN provides flexibility, customization, scalability for cloud computing, edge computing, fog computing, mobility, social networking, video streaming, augmented reality, virtual reality, vehicular area network….
SDN

## Slide 5
Control and Data Plane

## Slide 6
SDN Architecture

## Slide 7
Internet Society – (Organization)
  IETF – Internet Engineering Task Force - Working on protocols for end systems (Routing)
  IRTF – Internet Research Task Force – Provides useful information to APIs
ITU-T – International Telecommunication Union - (Organization)
  SG 11 – Study Group – Studying the framework for SDN signaling (Requirements, protocols and specifications)
  SG 13 – Working for Future Networks (Cloud Computing, Mobile computing, Edge computing, Next generation Networking)
  SG 15 – Working on Openness – Transportation aspect of SDN
  SG 16 – Working on Multimedia communication (Opnflow)
ETSI – European Telecommunications Standard Institute - (Organization)
  NFV ISG – Defines the standards for NFV
Standards-Developing Organizations

## Slide 8
Industry Consortia
ONF (Openflow)
ODCA (Working on interoperability solutions and provides the services for cloud computing)
Atis (Alliance for Telecommunication Industry) – Provides the tools for telecommunication services.

## Slide 9
Open Daylight – Main focus is on Linux – Provide resources to develop sdn controller
OpenFV – Focus is on NFV
Openstack – Working on Cloud OS – (Neutron service is working on SDN)
Open Development Initiatives

## Slide 10
Resource Layer
Infrastructure Layer
Network forwarding devices perform the transport and processing of data
  Data plane network elements/switches
According to decisions made by the SDN control plane.
These devices perform a simple forwarding function
SDN data plane

## Slide 11
SDN Data Plane Network Device

## Slide 12
Control Support Function
  Interacts with the SDN control layer.
Data forwarding function
  Accepts incoming data flows from other network devices and end systems and forwards them resource layer. (Based on rules)
SDN Data Plane Network Device - Functions

## Slide 13
To implement SDN, two requirements must be met.
A common logical architecture in all switches, routers, and other network devices.
  Managed by an SDN controller.
A standard, secure protocol is needed between the SDN controller and the network device.
These requirements are addressed by OpenFlow.
OpenFlow Logical Network Device

## Slide 14
OpenFlow Environment – OpenFlow switch context

## Slide 15
OpenFlow Switch

## Slide 16
Physical Ports : For Hardware interfaces – eg. Ethernet Interfaces
Logical Ports: Do not link to a hardware interfaces, higher level abstraction
Reserved Ports: Specify generic forwarding actions like sending to controller, flooding, forwarding using OpenFlow methods.
OpenFlow Ports

## Slide 17
OpenFlow channel
OpenFlow port
Flow table
Group table
Meter table
OpenFlow Switch

## Slide 18
OpenFlow Switch – Flow table structure

## Slide 19
A flow table consist of flow entries. The main components of a flow entry are as below:
Match fields : is used to match against packets. Consist of ingress port, packet header and optionally, metadata specified by previous table
Priority : Matching precedence of the flow entry
Counters: Updated when packets are matched
Instructions : to modify the action set
Timeouts : Maximum amount of time or idle time before flow is expired by switch
Cookie : May used by controller to filter flow entries affected by flow statistics, flow modification and flow deletion request. Not used when processing packets.
Flags : flags alter the way flow entries are managed
Flow Table

## Slide 20
If there is more than one flow table, they are organized as a pipeline
Provide the SDN controller with flexibility
Two stages of processing
  Ingress processing
  Egress processing
OpenFlow Switch – Flow table pipeline

## Slide 22
Packet processing starts at flow table 0
Packet is matched against the flow entries of the flow table
If a flow entry is found, the instruction set in that flow entry will execute
“GoTo Table Instruction” to direct the packet to another flow table
Pipeline can only go forward not backward
Table miss: when packet does not match a flow entry in a flow table
Table-miss packets can be dropped, pass them to another table or sending them to a controller
If there is not table-miss flow entry, the packet is dropped
Pipeline Processing

## Slide 23
Matching Process

## Slide 24
OpenFlow Switch – Use of multiple tables – Example of Nested Flows

## Slide 25
OpenFlow Switch – Group Tables

## Slide 26
OpenFlow defines both the communications protocol between the SDN data plane and the SDN control plane, as well as part of the behavior of the data plane.
General-purpose protocol for programming the forwarding plane of SDN switches.
Openflow.org in 2008 – Stanford University – (Experimental Version)
First version 1.0.0 in December, 2009 – (Development and Management)
Open Network Foundation (ONF) in March, 2011 – (Delivery)
OpenFlow remains at the core of their SDN.
ONF has become the responsible entity for the evolving OpenFlow specifications.
Overview of OpenFlow

## Slide 27
OpenFlow Switch – V.1.0

## Slide 28
OpenFlow Controller
Defines the communication between an OpenFlow controller and an OpenFlow switch.

## Slide 29
Controller-Switch secure channel

## Slide 30
Released on December 31, 2009.
Initial release of OpenFlow
OpenFlow 1.0

## Slide 31
OpenFlow 1.0 – Ports and Port Queues

## Slide 32
OpenFlow 1.0 – Flow Table
                Basic flow entry

## Slide 33
When a packet arrives at the OpenFlow switch from an input port (or Controller), it is matched against the flow table to determine if there is a matching flow entry.
Some fields are:
  Switch input port
  VLAN ID
  VLAN priority
  Ethernet source address
  Ethernet destination address
  Ethernet frame type
  IP source address
  IP destination address
  IP protocol
OpenFlow 1.0 – Packet Matching

## Slide 34
Five special virtual ports defined in V.1.0
  LOCAL
  ALL
  CONTROLLER
  IN_PORT
  TABLE
Two optional
  NORMAL
  FLOOD
OpenFlow 1.0 – Actions and Packet Forwarding

## Slide 35
OpenFlow 1.0 – Messaging Between Controller and Switch

## Slide 36
OpenFlow 1.0 – Messaging Between Controller and Switch

## Slide 37
Released on February 28, 2011.
OpenFlow 1.1

## Slide 38
Released on December 05, 2011.
OpenFlow 1.2

## Slide 39
Released on April 13, 2012.
OpenFlow 1.3

## Slide 40
Released on October 14, 2013
OpenFlow 1.4

## Slide 41
OpenFlow Version RoadMap
Feature-set comparison
MPLS – Multi-Protocol Label Switching
HA - High Availability

## Slide 42
Timeline

## Slide 43
Explain OpenFlow architecture and list down OpenFlow components
What are Control Plane (CP) and Data Plane (DP) in SDN?
What are the central tasks of the Data Plane with the forwarding hardware?
What is data plane and what does it contain?
List down OpenFlow versions.
Explain OpenFlow components in detail.
Assignment questions

## Slide 44
Thankyou